Space Systems Engineering

Topic: Cost Estimation and Use of Monte Carlo

HOMEWORK #7

Due: Two weeks from assigned

Type: Individual, written

Please submit in hard copy, including your code.

Documents to use in this assignment:

Small Satellite Cost Model (Aerospace Corp) – pdf file

NEAR Spacecraft and Instrumentation Data – pdf file

NASA Inflation Index Table – xls file

Aerospace Corp Development of the SSCM (paper for added reference) – pdf file

Part 1 – point estimate (40 points)

- Produce a cost estimate for the NEAR spacecraft (instruments not included). Show the detailed estimates for each subsystem and wrap factor.

- Populate a table with the cost estimate in (a) including the total cost, non-recurring cost, and recurring cost. This table should include the entire spacecraft, subsystems and wraps.

- Inflate the total spacecraft cost estimate to 2008 dollars using the NASA Inflation Index Table.

- Note any groundrules and assumptions for this part of the assignment.

Part 2 – probabilistic estimate (50 points)

- Using the table below, run a Monte Carlo on the NEAR spacecraft cost estimate in 2008 dollars. Use 10,000 for the number of runs. Document the nominal value for your input (this was needed in part 1 of the assignment).

| Monte Carlo Parameters and Variations |  |  |  |
| --- | --- | --- | --- |
| Parameter | Nominal | Distribution | Range |  |
|  | Value |  |  |  |
| Satellite wet mass |  | Uniform | ±20% | min/max |
| Pointing Knowledge |  | Normal | 0.001 degrees | 3-sigma |
| ADCS Subsystem mass |  | Uniform | ±20% | min/max |
| Propulsion Subsystem mass | Uniform | ±20% | min/max |
| Beginning of life power |  | Uniform | ±10% | min/max |
| C&DH Subsystem mass |  | Uniform | ±10% | min/max |
| Structural mass |  | Uniform | ±20% | min/max |
| Solar array area |  | Uniform | ±10% | min/max |
| Thermal Subsystem mass |  | Uniform | ±20% | min/max |
| Design Life |  | Normal | 24 months | 3-sigma |
| Bus dry mass |  | Uniform | ±20% | min/max |
| Development Time |  | Normal | 7 months | 3-sigma |

- Plot the Monte Carlo results as a PDF and a CDF (or “S” curve).

- Show the point estimate on the CDF and compare to the 65% confidence level.

- How much reserve (also known as margin) should be added to the point estimate to meet a 65% confidence level?

Part 3 – discussion (10 points)

Discuss the use of the Small Satellite Cost Model.

- Any concerns applying it to the NEAR spacecraft?

- Was the point estimate what you expected? Was its probability of occurrence what you expected?

- How would you recommend checking the reasonableness of your point estimate?

Notes and Hints:

- The solar array panel dimensions are incorrectly stated in the NEAR technical paper. The dimensions should be 1.83 x 1.22 m.

- Select the correct CERs for the NEAR mission type.

- Watch your units.

- Watch for wet vs dry mass.

- CER for C&DH accounts for cost of telecom subsystem, but does not include telecom subsystem mass.

- Suggestion: you may want to do Part 1 in Excel as a check on your programming the equations correctly in Matlab. You will need to use Matlab for Part 2. The Monte Carlo lecture notes provided a framework for the code.